## Slide 1
TBSC Safety Briefing
2026

## Slide 2
Commodore’s Annual Newsletter 2026
“… rescue can be intimidating but courses are invaluable. They teach seamanship, how to react in tricky conditions … how to look for and avert difficulties … learn about the tides, the dangerous rocks, the channels between them
It diminishes the danger when the wind erupts or the fog rolls in, and you can potentially save a call-out for the RNLI”

## Slide 3
“… when the wind erupts”

## Slide 4
RYA Youth Nationals, April 2025
“A sudden and rapid weather change resulted in high winds
Event’s designated rescue boats became overwhelmed by the number of young sailors requiring assistance
Initial reports indicated 15 people were unaccounted for
One adult safety crew sustained a head injury”

## Slide 5
Repeated capsizing
Inversion & entrapment
Injury
RIB handling error, potential propellor strike
In Trearddur Bay
Sea state is primary cause

## Slide 6
Look at primary risks
Propellor Strike
Medical Emergency
Entrapment … unaccounted for …
And … “how to react in tricky conditions” … and practical tips

## Slide 7: 1. Propellor Strike
Near miss – RIB drove over capsized dinghy
Probability low, consequences catastrophic

## Slide 8: RIB - safe handling
“One hand steer, one hand gear”
Manoeuvre: “Brain – steer – gear - throttle”
Close quarters: “Steer – gear – neutral – steer – gear”
Turn off engine when recovering people from water

## Slide 9
2. Medical Emergency
Beaumaris RC, Longboat rower became ill
Coxed to nearest Safe Haven
Location VHF Blackspot = mobile phone 999
Doctor & Ambulance … heart attack
Comms with “Flagstaff” … problem

## Slide 10
TBSC
Medical emergency procedure

## Slide 11
“Scoop and run” to nearest Safe Haven
Life threatening condition = Channel 16
“Mayday, Mayday, Mayday”
Non-emergency, inform Flagstaff nature of injuries – VHF relay if Blackspot
Area 1, land at RNLI slipway

## Slide 12
Area 3 Safe Haven

## Slide 13
3. Avert difficulties

## Slide 15
… Lobster pot ropes!
Onshore wind =
Lee Shore
Ebb tide creates tide rip Ravenspoint to Deadmans

## Slide 18
  Classes most at risk
  38x RS Fevas & 28x RS200s
    Risk of inversion & entrapment
    Low probability, high/catastrophic consequence
    Masthead float reduces probability
  49x Myths
    Risk fill & swamp, carried onto rocks
    Medium probability, medium/high consequence
    Buoyancy bags reduce probability

## Slide 19
  Entrapment
  RS400 crew’s leg tangled in Half Rater main sheet
  Inverted dinghy, first RIB attending, crew headcount
    Release trapped crew … enter water if necessary
    If injury, scoop & run to nearest safe haven
    VFH comms with Flagstaff
  Pre-departure, knife to hand, wire cutters from rescue bucket

## Slide 20
  Recommend all sailors and rescue crew wear a personal rescue knife attached to their PFD or belt – able to cut Dyneema or Spectra

## Slide 21
Crew tired/cold? Shock?
Instruct dinghy crew to board RIB
  Assess condition
  If abandoning dinghy, report Sail Number to Flagstaff
  Take crew ashore
Recover dinghy?
  Not priority during racing

## Slide 22
Crew on Lee Shore rocks
Professional Safety Boat crews or RNLI
Most likely a Myth on Lagoon or Cod Rocks …
Risk of crew injury lower leg, arms
Safety RIB position upwind, deploy anchor
Engine in neutral
Let out anchor line, stay clear of outlying rocks
Throw-bag heaving line
Pull crew to Safety Boat
TURN ENGINE OFF
Recover dinghy crew

## Slide 23
Righting inverted RS in seaway
Advanced RIB handlers only
Take crew into RIB … downwind side
Position RIB upwind, stern to waves, hold station in reverse gear
Attach 2 ropes
    One from bow of RIB to bow of RS
    Pass other across hull attach to righting line or jib sheet
    May need 2nd RIB to assist

## Slide 25
Advice
  When first checking in with Flagstaff, RIB helm report engine Kill Cord is attached to their leg
  Kill Cord worn at all times
  RS Feva main halyard cleated at top of mast, if capsized rescue crew release halyard or cut it
  If dinghy capsized with Spinnaker up, rescue crew hold top of mast to prevent inversion whilst crew untangle Spinnaker and lines

## Slide 26
Reminders
Wear PFDs and gloves
Constant 360 lookout
Risk of swamping reversing into waves
  Depends on RIB’s design
  Trim engine up before reversing!
Towing astern
  Sails down, centreboard up, crew weight aft & steering

## Slide 27
Towing alongside for control and close quarters manoeuvring of heavy or partially filled boat

## Slide 29: Engine failure … rescue RIB?
Contaminated fuel
Kill Cord or isolator switch overboard
Lobster pot rope round prop

## Slide 30
Test or check: VHF operation, anchor ready, pump and buckets, MoB recovery method, first aid kit, knife, wire cutters, fire extinguisher, drinking water…
Arrangements for towing astern and alongside
Crew briefing and emergency procedures
Pre-departure check list